I-M.Tech(CSE)-DSP(1.3)

M.Tech(CSE) 1st Semester  Examination -2019

Sub: Digital Signal Processing

Full Mark – 70								Time: 3Hrs

(Answer all questions. Figure in the right hand margin indicate marks.)

- (a) A discrete time signal x(n) is defined as

x(n) = |n- 0.5|,    –3 ( n ( 3

0       ,    otherwise

(i)  Sketch the signal x(n).  (ii) Find  x(-n + 2)  (iii) Find x(n). u(-n-1).            [5]

(b) Determine whether the system given by input-output relation y(n) = 5x(-n) is time-variant or time-invariant.					                   [4]

(c) The impulse response of a LTI system is h(n) = (1/2)n u(n). Determine the response of the system to the input signal x(n) = (1/4)n u(n). 	                   [5]

OR

- How to determine the stability of a LTI system from its impulse response? Determine range of  b for which the system with impulse response

h(n) =  	bn , n < 0 to be stable. 						       [7]

- Determine convolution of the two signals given by

x1(n) = ((n) + 3((n-2) + 2((n-1) and x2(n) = ((n+1) + ((n-1) - ((n+2).	       [7]

- (a) Determine the zero input response of the system described by 2nd order difference equation

y(n) - 3 y(n-1) - 4 y(n-2) = x(n). Consider y(-1) = 5, y(-2) = 0	     [10]

- Determine the cross correlation of two sequences

x1(n) = u(n+1) – u(n-2) and x2(n) = {1,-1,2,1}			                   [4]

OR

Determine the response y(n) for the system described by 2nd order difference equation y(n) - 3y(n-1) - 4 y(n-2) = x(n) + 2x(n-1) where the input sequence is x(n) = 4n u(n). Consider y(-1) = 5, y(-2) = 0			                             [14]

3.    (a) State and prove the convolution property of z-transform.                               [7]

(b) Consider a initially relaxed LTI system described by difference equation

y(n) =  0.25 y(n-2) + x(n). Determine the system function and impulse response of the system.      								       [7]

OR

- Find inverse z-transform of X(z) = 1 / {(1 + z-1) (1 + z-1)2}.		       [7]

- Find inverse z-transform using long division method of

X(z) = 1 / (1 – 1.5z-1 + 0.5z-2)  if ROC:  |z| < 0.5.		                   [7]

4.    Perform the circular convolution of two sequences using both time domain and frequency domain method. Verify your result using matrix method.

x1(n) = {2,-1,2,-1} and x2(n) = {1,2,3,4}		                [6+6+2=14]

OR

(a) Find DFT of the sequence x(n) = {1,2,-1,2} using linear transformation method.			                   					       [5]

(b) Determine the DFT transformation matrix for N =8. 			       [5]

(b) State and prove the complex conjugate property of discrete Fourier transform.		                  								       [4]

5. (a) An FIR filter has unit impulse response h(n) = {2,2,1}. Determine the output sequence in response to input sequence x(n) = {3,0,-2,0,2,1,0,-2,-1,0} using overlap add method.							                 [10]

(b) A sequence is given by x(n) = n+1 for 0 ≤ n < 4. Find the discrete Fourier transform using Decimation – in – frequency FFT algorithm.	                   [4]

OR

- Determine the direct form II realization of LTI system given by

y(n) + 3y(n-1) – 4 y(n-3) = x(n) + 2 x(n-4)				      [7]

- Draw the butterfly structure of an 8-point FFT using Decimation – in –      time algorithm.     					       		       	      [7]